## Slide 1: Blackjack Military Space Pivot to LEO
Mr. Paul “Rusty” Thomas, Program Manager
DARPA Tactical Technology Office
Briefing prepared for Future In-Space Operations Telecon
August 22, 2018

## Slide 2: Military Space - Pivot to Low Earth Orbit (LEO)
LEVERAGE:
Commercial LEO
Mega-Constellation
Global “Space Internet”
High-speed crosslinks
Launch, operations,
and ground
infrastructure in place
DEVELOP:
Co-Orbiting Military
Demo Constellation
Rapid tech refresh
Resilience
Global persistence
Autonomous ops
Overhead Persistent Infrared (OPIR) Position Navigation Timing (PNT) Communication (RF)
Low-cost commoditized COTS bus
Rapid response to future threats
Commercial
Network
Satellite
Military
Satellite
Demonstrate a space order of battle architecture that cannot be easily defeated by a near peer, and enables one to two year technology refresh cycles vs current 10 year cycles.
Artist’s Concept

## Slide 3: 20 LEO Autonomous Spacecraft Demonstration
Global coverage
Commercial launch capability to launch 2 military S/C per week
Full system could launch in 2022
90-Spacecraft Objective System
9 planes x 10 sats/plane
(not part of Blackjack program)
20-Spacecraft Demonstration
2 planes x 10 sats/plane at 1000 km
(2 s/c initially plus 18 add’l for full demo)
  Demonstrate:
  Persistence – spacecraft handoff
  Autonomy
  Network / crosslinks
  On-board processing
  Stereo sensing
  Global Command, Control, Commun- ications (C3)
  Commercial Production Line Approach
Coverage footprint would enable simultaneous theater-level demos
Notional orbits/inclination
Notional

## Slide 4: Commercial Mega-Constellation in LEO for Global “Space Internet”
(45 degree grazing angle=10+ satellites in view)
Commercial LEO
Mega-Constellations
Concepts with hundreds to thousands of LEO comm satellites
Commoditized Bus
Inter-satellite Links
Frequent
launches
Constellation management
Leverage Commercial Investment
20+
s/c
1
2
3
4
Unprecedented low cost: Bus: $1M-5M; Payload: $1M-5M; Launch: $2M-5M
2021 demo (planned): 20 autonomous spacecraft in 2 orbital planes for theater-level ops
1-3 wks
…
…
1-3 wks
20+
s/c
20+
s/c
…
…
200+ Satellites in View
From Single Ground Point
(0 degree grazing angle shown)

## Slide 5: Cost Objective: Blackjack
Military Benefits
Resilience
Deterrence
Launch: $3M/satellite x 90
= $270M
Payload: $2M x 90
= $90M
= $180M
Std Bus: $1M x 90
Cost of One SBIRS GEO
Cost of Notional LEO
OPIR Constellation
Rapid tech refresh
Global persistence
Scalable
Tactical timelines
Spacecraft + Launch: $1.2B
CONSTELLATION COST
$540M

## Slide 6: Program Technology Challenges
    Demonstrate payload autonomy
        Auto Target Recognition and geolocation
        Tactical- and operational-level direct prioritization
    Demonstrate multi-theater mission autonomy
        Develop human-on-the-loop verification schemes for space C3ISR
    Demonstrate DoD can maintain commercial pace
    Flight readiness to LEO operations in weeks
      Annual tech refresh cycle
    Interface Control Document (ICD) to manage commercial configurations
    Demonstrate capability of OPIR/PNT/RF systems to augment NSS systems without exquisite payload cost and schedule
    Prove pivot to LEO as optimal architecture to expand NSS capabilities and quickly respond to new threats
Payload Manufacturing Technology
LEO Constellation Performance
Autonomy and
On-Orbit Decisions
Artist’s Concept

## Slide 7: LEO Mission Payload Advantages
Signal strength at LEO is 1280x stronger than at geosynchronous orbit (GEO)
Low latency in LEO improves tactical timelines
Persistence via proliferation across LEO constellation – continuous coverage
Mission | OPIR | PNT | Comm | RF | Radar
LEO Impact (Envisioned) | Augment missile warning/defense | Augment GPS | Global comm/ tactical timelines | Increased signal strength | Global coverage
LEO
GEO
Signal: +31dB vs GEO
14 ms
478 ms
Launch: ~$5,000/kg
Launch: ~$30,000/kg
Signal: weak
COTS
BUS
P/L

## Slide 8: Blackjack Schedule
Demo coverage footprint for 2 planes,
10 satellites/plane, 1000 km
20-satellite demonstration
Notional orbits/inclination